## Slide 1: Application of Nuclear Physics
Frontier of gamma-ray spectroscopy
energy [eV]
1
1e4
1e5
1e6
10
100
1e3
0.1
IR visible light UV soft X-ray X-ray hard X-ray gamma-ray →
Germanium
semi-conductor detectors
Photoelectric effect
Compton scattering
e-
e-

## Slide 2: Why imaging gamma-rays?
High energy astrophysics
Correlate the detected photon to source object as known
from more precise observations in other wavelength
Biomedical research
Precise localization of radioactive tracers in the body
Cancer diagnosis
Molecular targeted radiation therapy
Monitor changes in the tracer distribution → dynamic studies
National security
Nuclear non-proliferation / nuclear counter terrorism
Contraband detection
Stockpile stewardship
Nuclear waste monitoring and management
Industrial non-destructive assessments
Determination of the material density distribution
between the source and detector

## Slide 3: Application of Nuclear Physics
First X-ray image by Wilhelm Conrad Roentgen (1895)
Standard X-ray imaging
Absorption of X-rays by bones and transmission through soft tissue produces image
What if we want a 3D image?
What if we want detailed information on organs, bones and muscles etc?
Nobel Prize 1901

## Slide 4: Tomographic Imaging
PET
SPEC
CT
OPTICAL
MRI

## Slide 5: Computed Tomography
CT scanning (originally known as CAT)
X-rays taken at a range of angles around the patient
Generation of 3D images
Radiation detector
X-ray source
Standard CT-system

## Slide 6: Positron Emission Tomography

## Slide 7: Positron emission tomography

## Slide 8: Common PET Isotopes

## Slide 9: PET Isotopes: Positron Range

## Slide 10: Single Photon Emission Computed Tomography
Most commonly used tracer in SPECT is 99Tcm, 140 keV a pure single photon emitter T1/2 = 6.02 h.
Utilizes a gamma-ray camera rotated in small ~30 steps around the patient.

## Slide 11: Technetium- 99m
Supplied in a generator consisting of 99Mo absorbed onto alumina.
Container allows liquid introduced at top to be collected at bottom.
Needs replacing weekly

## Slide 12: The motivation behind the project
Existing technology relies on BGO scintillator technology
- Limited position resolution
- High patient dose requirement.
- Poor energy resolution only accept photopeak events.
- Will not function in large magnetic field
SPECT applications utilizing Compton Camera techniques.

## Slide 13: Which γ-ray camera to be used?
Requirements:
Excellent resolution Δx = 2 mm
Large field of view (FOV) = 8x9 cm2
www.siemens.de
Large FOV of ~20 cm diam.
Low spatial resolution 0.5-1 cm
Small FOV of 3-4 cm diam.
High spatial resolution 2-3 mm
Gem-imaging.com

## Slide 14: Gamma Camera: Individual multi-anode readout
16 wires in X axis and 16 wires in Y axis
Hamamatsu R2486 PSPMT
Photocathode = 56.25 mm
d = 76 mm
t = 3 mm
ρ = 7.4 g/cm3
LYSO
scintillator
C.Domingo Pardo, N. Goel, et.al., IEEE, Vol.28, Dec. 2009

## Slide 15: Which γ-ray camera to be used?
Small FOV of 3-4 cm diam.
High spatial resolution 2-3 mm
Gem-imaging.com
Requirements:
Excellent resolution Δx = 2 mm
Large field of view (FOV) = 8x9 cm2
Scintillator
Position Sensitive
PMT

## Slide 16: Which γ-ray camera to be used?
Small FOV of 3-4 cm diam.
High spatial resolution 2-3 mm
Gem-imaging.com
Requirements:
Excellent resolution Δx = 2 mm
Large field of view (FOV) = 8x9 cm2
Scintillator
Position Sensitive
PMT
g-ray

## Slide 17: Which γ-ray camera to be used?
Small FOV of 3-4 cm diam.
High spatial resolution 2-3 mm
Gem-imaging.com
Requirements:
Excellent resolution Δx = 2 mm
Large field of view (FOV) = 8x9 cm2
Scintillator
Position Sensitive
PMT
g-ray

## Slide 18: Which γ-ray camera to be used?
Small FOV of 3-4 cm diam.
High spatial resolution 2-3 mm
Gem-imaging.com
Requirements:
Excellent resolution Δx = 2 mm
Large field of view (FOV) = 8x9 cm2
Scintillator
Position Sensitive
PMT
g-ray

## Slide 19: Which γ-ray camera to be used?
Small FOV of 3-4 cm diam.
High spatial resolution 2-3 mm
Gem-imaging.com
Requirements:
Excellent resolution Δx = 2 mm
Large field of view (FOV) = 8x9 cm2
Scintillator
Position Sensitive
PMT
g-ray
g-ray 2

## Slide 20: Gamma-ray tracking – the concept
without Compton suppression shield
with BGO shielding
with highly segmented detectors
Compton continuum → small peak to total ratio
Less solid angle coverage → big drop in efficiency
Path of γ-ray reconstructed to form full energy event
→ Compton continuum reduced
→ Excellent efficiency ~50% @ 1 MeV
→ Greatly improved angular resolution (~1%)
to reduce Doppler effect.

## Slide 21: HPGe detector – working principle

## Slide 22: HPGe detector – working principle
+ HV = 4000 Volts
E = -V V

## Slide 23: HPGe detector – working principle
+ HV = 4000 Volts
E = -V V
g-ray
electrons
holes

## Slide 24: HPGe detector – working principle
+ HV = 4000 Volts
E = -V V
electrons
holes
Electric signal
g-ray

## Slide 25: HPGe detector – working principle
+ HV = 4000 Volts
E = -V V
electrons
holes
Electric signal
g-ray

## Slide 26: HPGe detector – working principle
+ HV = 4000 Volts
E = -V V
electrons
holes
Electric signal
g-ray

## Slide 27: HPGe detector – working principle
+ HV = 4000 Volts
E = -V V
electrons
holes
Electric signal
g-ray
g-ray 2

## Slide 28: HPGe detector – working principle
+ HV = 4000 Volts
E = -V V
electrons
holes
Electric signal
g-ray

## Slide 29: Characterization of planar HPGe detector
Front view
Side view
Planar Ge
d = 4 cm
t = 2 cm
22Na
Position sensitive detector

## Slide 30: Planar HPGe detector scan
(a)
(b)
Intensity distribution for photopeak events
t(ns)
amplitude, Φ
t(ns)

## Slide 31: Outlook
?
M.J. French et al., NIMA 466 (2001) 359
APV25 chip (from CERN CMS experiment)
128-channel analogue pipeline chip
The GSI system uses conventional NIM and VME electronics, which makes it not easily portable, not easily scalable and rather expensive if one wants to build many of these devices.
However, this drawback could be overcome thanks to the increasing technology of electronics, e.g. a new acquisition system based on ASIC, FPGA, etc. technologies. This would also make the system more suitable for medical applications.

## Slide 32: Position Extraction in Planar Detectors

## Slide 33: Position Extraction in Planar Detectors

## Slide 34: Gamma-Ray Imaging
Gamma-ray imagers are detectors that separate radioactive objects from local background.
Conventional detectors accept gamma-rays from all directions and can be overwhelmed by local backgrounds.