## Slide 1: Past / Future in Scintillation
Lecture: Hans-Jürgen Wollersheim
e-mail: h.j.wollersheim@gsi.de

## Slide 2: Past / Future in Scintillation
High energy astrophysics
Correlate the detected photon to source object as known
from more precise observations in other wavelength
Biomedical research
Precise localization of radioactive tracers in the body
Cancer diagnosis
Molecular targeted radiation therapy
Monitor changes in the tracer distribution → dynamic studies
National security
Nuclear non-proliferation / nuclear counter terrorism
Contraband detection
Stockpile stewardship
Nuclear waste monitoring and management
Industrial non-destructive assessments
Determination of the material density distribution
between the source and detector

## Slide 3: Past / Future in Scintillation
Afterglow = phosphorescence
Phosphorescence is a property of many crystals and organic materials
Light is produced by deexcitation of molecules

## Slide 4: Zinc Sulfide ZnS(Ag) Scintillation Material
1866 – Theodore Sidot reported the phosphorescence of ZnS.
1903 – William Crookes invented a device called a spinthariscope
with a ZnS screen to see scintillations from α-particles.
In 1903 W. Crookes demonstrated in England his
“spinthariscope” for the visual observation of individual
scintillations caused by α-particles impinging upon a ZnS screen. In contrast to the analogue methods of radiation measurements in that time the spinthariscope was a single particle counter, being the precursor of scintillation counters since. In the same period F. Giesel, J. Elster and H. Geitel in Germany also found that scintillations from ZnS represent single particle events. This paper summarizes the historical events relevant to the advent of scintillation counting.
A spinthariscope from 1904. Height about 5 cm, Ra-source (A), ZnS screen (B), magnifying glass

## Slide 5: Zinc Sulfide ZnS(Ag) Scintillation Material
1944 – photomultiplier tube was invented
α-particles
γ-rays
β-particles
background pulses
of naphtalene -200
1948 – H. Kallmann

## Slide 6: History of Scintillators
year of introduction of a scintillation material
History of scintillators starts short after the discovery of X-rays at the end of 19th century

## Slide 7: Compton Suppression Shields NaI(Tl) versus BGO
material | NaI(Tl) | BGO
density (g/cm3) | 3,67 | 7.13
50% attenuation for 662 keV in cm | 2.5 | 1.0
Index of refraction n | 1.85 | 2.15
Emission (photons/keV) | 38 | 8
Decay time (ns) | 250 | 300
Maximum size grown (mm) | 700 | 75
Radioactive contamination | 40K | 207Bi
NaI(Tl)
BGO

## Slide 8: Heidelberg – GSI Crystal Ball
NaI(Tl)
Ge(Li)
~160 NaI(Tl) and 5 EUROBALL detectors

## Slide 9: Tomographic Imaging
PET
SPEC
CT
OPTICAL
MRI

## Slide 10: Computed Tomography
CT scanning (originally known as CAT)
X-rays taken at a range of angles around the patient
Generation of 3D images
Radiation detector
X-ray source
Standard CT-system

## Slide 11: Positron Emission Tomography

## Slide 12: Positron emission tomography

## Slide 13: Common PET Isotopes

## Slide 14: PET Isotopes: Positron Range

## Slide 15: Single Photon Emission Computed Tomography
Most commonly used tracer in SPECT is 99Tcm, 140 keV a pure single photon emitter T1/2 = 6.02 h.
Utilizes a gamma-ray camera rotated in small ~30 steps around the patient.

## Slide 16: Technetium- 99m
Supplied in a generator consisting of 99Mo absorbed onto alumina.
Container allows liquid introduced at top to be collected at bottom.
Needs replacing weekly

## Slide 17: The motivation behind the project
Existing technology relies on BGO scintillator technology
- Limited position resolution
- High patient dose requirement.
- Poor energy resolution only accept photopeak events.
- Will not function in large magnetic field
SPECT applications utilizing Compton Camera techniques.

## Slide 18: Which γ-ray camera to be used?
Requirements:
Excellent resolution Δx = 2 mm
Large field of view (FOV) = 8x9 cm2
www.siemens.de
Large FOV of ~20 cm diam.
Low spatial resolution 0.5-1 cm
Small FOV of 3-4 cm diam.
High spatial resolution 2-3 mm
Gem-imaging.com

## Slide 19: Gamma Camera: Individual multi-anode readout
16 wires in X axis and 16 wires in Y axis
Hamamatsu R2486 PSPMT
Photocathode = 56.25 mm
d = 76 mm
t = 3 mm
ρ = 7.4 g/cm3
LYSO
scintillator
C.Domingo Pardo, N. Goel, et.al., IEEE, Vol.28, Dec. 2009

## Slide 20: Which γ-ray camera to be used?
Small FOV of 3-4 cm diam.
High spatial resolution 2-3 mm
Gem-imaging.com
Requirements:
Excellent resolution Δx = 2 mm
Large field of view (FOV) = 8x9 cm2
Scintillator
Position Sensitive
PMT

## Slide 21: Which γ-ray camera to be used?
Small FOV of 3-4 cm diam.
High spatial resolution 2-3 mm
Gem-imaging.com
Requirements:
Excellent resolution Δx = 2 mm
Large field of view (FOV) = 8x9 cm2
Scintillator
Position Sensitive
PMT
g-ray

## Slide 22: Which γ-ray camera to be used?
Small FOV of 3-4 cm diam.
High spatial resolution 2-3 mm
Gem-imaging.com
Requirements:
Excellent resolution Δx = 2 mm
Large field of view (FOV) = 8x9 cm2
Scintillator
Position Sensitive
PMT
g-ray

## Slide 23: Which γ-ray camera to be used?
Small FOV of 3-4 cm diam.
High spatial resolution 2-3 mm
Gem-imaging.com
Requirements:
Excellent resolution Δx = 2 mm
Large field of view (FOV) = 8x9 cm2
Scintillator
Position Sensitive
PMT
g-ray

## Slide 24: Which γ-ray camera to be used?
Small FOV of 3-4 cm diam.
High spatial resolution 2-3 mm
Gem-imaging.com
Requirements:
Excellent resolution Δx = 2 mm
Large field of view (FOV) = 8x9 cm2
Scintillator
Position Sensitive
PMT
g-ray
g-ray 2

## Slide 25: Gamma-ray tracking – the concept
without Compton suppression shield
with BGO shielding
with highly segmented detectors
Compton continuum → small peak to total ratio
Less solid angle coverage → big drop in efficiency
Path of γ-ray reconstructed to form full energy event
→ Compton continuum reduced
→ Excellent efficiency ~50% @ 1 MeV
→ Greatly improved angular resolution (~1%)
to reduce Doppler effect.

## Slide 26: Scanner at GSI
Characteristics:
Faster
Precision: 1-2 mm
Imaging capability
Requirements:
1. Position sensitive detector
- Excellent Δx/x
- Large field of view
2. Method to compare the pulses
Rotating table
Position sensitive detector
22Na

## Slide 27: Position calibration
Determine: Xr(xm,ym), Yr(xm,ym)
Gamma-ray scattering technique
Grid raw image when it is parallel to PSD surface (0 deg)
00 position

## Slide 28: Position reconstruction
LYSO =76 mm
Photocathode=56.26 mm
Central Interaction
Peripheral Interaction
C. Domingo Pardo, N.Goel, et.al., IEEE, Dec. 2009 Volume: 28 Issue 12
average charge profile at the center
Reference peak fitting
Charge (a.u.)
Charge (a.u.)
Y (mm)
Y (mm)
C.W.Lerche, et.al., NIM A, Vol 537, pp. 326-330, Jan. 2005

## Slide 29: Position reconstruction
Gaussian fitting
Reference peak fitting
Linear for 50 mm
Field of view = 28 cm2
Pos. X (mm)
Gaussian fitting works relatively well in the central region
Average spatial resolution in X and Y ~ 1mm
Pos. X (mm)

## Slide 30: Scanner at GSI
Characteristics:
Faster
Precision: 1-2 mm
Imaging capability
Requirements:
1. Position sensitive detector
- Excellent Δx/x
- Large field of view
2. Method to compare the pulses
Rotating table
Position sensitive detector
22Na

## Slide 31: Superiority over conventional scanner
Advantage over conventional scanner: Full detector can be scanned in one measurement 10 times faster than a conventional scanner Accuracy of simulations can be checked for complex regions of electric field
BGO
BGO
coincidence between the Germanium and BGO detectors for 90 degree Compton scattered events for depth determination
137Cs

## Slide 32: Scanner based on pulse shape comparison scan
a)
a)

## Slide 33: Scanner based on pulse shape comparison scan
a)
b)
b)
Geometric crossing point: x,y,z
Common pulse out of data sets (a) & (b)
a)
Collimated source
F.C.L. Crespi, et al. NIM A 593 (2008), 440

## Slide 34: Pulse shape comparison scan method based on a position sensitive detector
22Na
Position sensitive
detector
a)
b)
Rotated by 900
Recording pulse shapes for positions (a) and (b)
Identical signals at the crossing point.
511 keV
22Na

## Slide 35: minimization method
0° measurement
t(ns)
t(ns)
amplitude, Φ
distribution
t(ns)
amplitude, Φ
Average pulse
amplitude, Φ
threshold
90° measurement

## Slide 36: Characterization of planar HPGe detector
Front view
Side view
Planar Ge
d = 4 cm
t = 2 cm
22Na
Position sensitive detector

## Slide 37: Detector scan
Front view (0 deg):
Side view (90 deg):

## Slide 38: Detector scan
Front view (0 deg):
Side view (90 deg):

## Slide 39
Detector scan (data analysis)

## Slide 40
Experimental validation of the method

## Slide 41: Planar HPGe detector scan
(a)
(b)
Intensity distribution for photopeak events
t(ns)
amplitude, Φ
t(ns)

## Slide 42: Outlook
?
M.J. French et al., NIMA 466 (2001) 359
APV25 chip (from CERN CMS experiment)
128-channel analogue pipeline chip
The GSI system uses conventional NIM and VME electronics, which makes it not easily portable, not easily scalable and rather expensive if one wants to build many of these devices.
However, this drawback could be overcome thanks to the increasing technology of electronics, e.g. a new acquisition system based on ASIC, FPGA, etc. technologies. This would also make the system more suitable for medical applications.

## Slide 43: Position Extraction in Planar Detectors

## Slide 44: Position Extraction in Planar Detectors

## Slide 45: Gamma-Ray Imaging
Gamma-ray imagers are detectors that separate radioactive objects from local background.
Conventional detectors accept gamma-rays from all directions and can be overwhelmed by local backgrounds.