## Slide 1: Particle and Radiation Detectors: Advances & Applications
Lecture: Hans-Jürgen Wollersheim
e-mail: h.j.wollersheim@gsi.de

## Slide 2: Particle Interaction with Matter
Aurora Borealis
Ionization

## Slide 3: Particle Interaction with Matter
Cherenkov Light
Characteristic glow from a reactor
Cherenkov radiation is an effect similar to sonic booms when the plane exceeds the velocity of sound

## Slide 4: Particle Interaction with Matter
Bremsstrahlung
Bremsstrahlung or ‘braking radiation’
Spectrum of the X-rays emitted by an X-ray tube with a rhodium target, operated at 60 kV. The continuous curve is due to bremsstrahlung, and the spikes are characteristic K lines for rhodium.

## Slide 5: Energetic charged particles in matter
Three types of electromagnetic interactions:
Ionization (of the atoms of the transversed material)
Emission of Cherenkov light
Emission of transition radiation
1) Interaction with the atomic electrons. The incoming particle looses energy and the atoms are excited or ionized.
2) Interaction with the atomic nucleus. The particle is deflected (scattered) causing multiple scattering of the particle in the material. During this scattering a Bremsstrahlung photon can be emitted.
3) In case the particle’s velocity is larger than the velocity of light in the medium, the resulting EM shockwave manifests itself as Cherenkov Radiation. When the particle crosses the boundary between two media, there is a probability of the order of 1% to produce an X-ray photon, called Transition Radiation.

## Slide 6: Measurement Principles
A particle detector is an instrument to measure one or more properties of a particle …
Properties of a particle |  | Type of detection principle:
- position and direction |  | position and tracking
- momentum |  | tracking in a magnetic field
- energy |  | calorimetry
- mass |  | spectroscopy and PID
- velocity |  | Cherenkov radiation or time of flight
- transition radiation |  | TRD
- spin, lifetime |  | 
Properties of a particle |  | Type of detection principle:
- position and direction |  | position and tracking
- momentum |  | tracking in a magnetic field
- energy |  | calorimetry
- mass |  | spectroscopy and PID
- velocity |  | Cherenkov radiation or time of flight
- transition radiation |  | TRD
- spin, lifetime |  | 

## Slide 7: Detection and Identification of Particles
Detection = particle counting (is there a particle?)
Identification = measurement of mass and charge of the particle
(most elementary particle have )
How:
- charged particles are deflected by B fields such that:
- particle velocity measured with time-of-flight (ToF) method
ToF for known distance
Ionization
Cherenkov radiation
Transition radiation

## Slide 8: Detection and Identification of Particles
Detection = particle counting (is there a particle?)
Identification = measurement of mass and charge of the particle
(most elementary particle have )
How:
- kinetic energy determined via a calorimetric measurement
- for Z=1 the mass is extracted from and
- to determine Z (particle charge) a Z-sensitive variable is e.g. the ionization
energy loss
a = material-dependent constant

## Slide 9: Relevant Formulae
The relevant formulae are calculated if A1, Z1 and A2, Z2 are the mass number (amu) and charge number of the projectile and target nucleus, respectively, and Tlab is the laboratory energy (MeV)
beam velocity:
Lorentz contraction factor:

## Slide 10: Some Nuclear Units
Nuclear energies are very high compared to atomic processes, and need larger units. The most commonly used unit is the MeV.
1 electron Volt = 1 eV = 1.6·10-19 Joules
1 MeV = 106 eV; 1 GeV = 109 eV; 1 TeV = 1012 eV
However, the nuclear size are quite small and need smaller units:
Atomic sizes are on the order of 0.1 nm = 1 Angstrom = 10-10 m. Nuclear sizes are on the order of femtometers which in the nuclear context are usually called fermis:
1 fermi = 1 fm = 10-15 m
Atomic masses are measured in terms of atomic mass units with the carbon-12 atom defined as having a mass of exactly 12 amu. It is also common practice to quote the rest mass energy E=m0c2 as if it were the mass. The conversion to amu is:
1 u = 1.66054·10-27 kg = 931.494 MeV/c2
electron mass = 0.511 MeV/c2; proton mass = 938.27 MeV/c2; neutron mass = 939.56 MeV/c2
Mass data: www-nds.iaea.org/amdc/ (mass16.txt)

## Slide 11: Measurement Principles
A measurement requires an interaction of the particle with the material of the detector. The interaction provokes two effects:
1st Creation of a detectable signal, e.g.
ionization → charges
excitation → scintillation
excitation of phonons → heat
2nd Alternation of the particles properties, e.g.
energy loss
change of trajectory due to scattering
absorption
unwanted side effects. They need to be as small as possible and well understood.

## Slide 12: Energy loss – dE/dx
Particles interact differently with matter. Important for detectors is the energy loss per path length. The total energy loss per path length is the sum of all contributions.
Depending on the particle type, the particle energy and the material some processes dominate, other do not occur. For instance only charged particles will interact with electrons of atoms and produce ionization, etc.

## Slide 13: Interaction with matter
accelerated motion:

## Slide 14: Interaction with matter
Bragg-curve
energy loss
range
d [cm]

## Slide 15: Energetic charged particles in matter
Hans Bethe
(1906-2005)
dominant in the classical limit [40 MeV/A (0.3c) - <1% deviation

## Slide 16: Energetic charged particles in matter
William Henry Bragg
(1890-1971)
Bragg curve

## Slide 17: Bethe-Bloch – Classical Derivation (Bohr 1913)
Gauss law (infinite cylinder, electron in center):

## Slide 18: Bethe-Bloch – Classical Derivation (Bohr 1913)

## Slide 19: Bethe-Bloch – Classical Derivation (Bohr 1913)

## Slide 20: Bethe-Bloch – Classical Derivation (Bohr 1913)

## Slide 21: Energetic charged particles in matter
Charged particle identification with
segmented or stacked detectors
Si

## Slide 22: Interaction of α-particles in matter
α-particles are highly ionized and lose their energy very fast by ionization and excitation
when passing through matter.
maximum energy transfer Tmax of a projectile with mass m
and velocity β on an electron me at rest
for all heavy primary particles except electrons and positrons
number of α-particles
as a function of distance x
energy loss of
α-particles
per distant unit
average range <R> of α-particles with 5 MeV
2,5cm in air, 2,3cm in Al, 4,3cm in tissue

## Slide 23: Energy loss and range of charged particles
-dE/dε is independent of the material for equal particles
the average range for particles with kin. energy T is obtained by integration
7.7 MeV α-particles in air:
range is not exact but there is range straggling,
the number of interactions is a statistical process.
energy loss
distance
5.5 MeV α´s in air
deuteron beam scintillating in air
Several empirical and semi-empirical formulae have been proposed to compute range of α-particles in air.
Scaling the range of other materials

## Slide 24: Interaction of charged particles in matter
Bethe-Bloch formula describes the energy loss of heavy particles passing through matter
Na : Avogadro number 6.02·1023 mol-1
re : class. electron radius 2.81·10-13 cm
me : electron mass
ρ : density of abs. matter
Z : element number of abs. matter
A : mass of abs. matter
z : charge number of incoming particle
Wmax : max. energy transfer in a single collision
I : average ionization potential
for small β the term 1/β2 is dominant
dE/dx has a minimum at βγ~3-4 (minimum ionizing particle)
for high momenta dE/dx reaches a saturation
= 0.3071 MeV g-1cm2

## Slide 25: Interaction of charged particles in matter
Bethe-Bloch formula describes the energy loss of heavy particles passing through matter
for small β the term 1/β2 is dominant
dE/dx has a minimum at βγ~3-4 (minimum ionizing particle)
for high momenta dE/dx reaches a saturation
= 0.3071 MeV g-1cm2
liquid-H2
He-gas
Specific energy loss rate
for muons, pions and protons in different materials
Dependence on mass A, charge Z of target nucleus
Minimum ionization: 1-2 MeV/g cm-2 [H2: 4 MeV/g cm-2]

## Slide 26: Energy loss of charged particles – dE/dx for different particles
for heavy particles in this momentum regime is well described by Bethe-Bloch formula, i.e. the dominant energy loss is collisions with atoms
for electrons does not follow Bethe-Bloch formula. The dominant process is Bremsstrahlung
[ALICE TPC, 2009]
momentum p (GeV/c)
TPC signal (a.u.)

## Slide 27: Example: Proton in Silicon
Bethe-Bloch formula describes the energy loss of heavy particles passing through matter
= 0.3071 MeV g-1cm2
dE/dx vs. E of protons in silicon

## Slide 28: Interaction of β-particles with matter
β-particles are also ionizing, similar to α-particles. Since the mass of the electrons and positrons are very small, the energy transfer per collision is small and the range large. Similar to the X-rays there is first only an attenuation, which finally leads to a maximum range for larger layer thicknesses.
layer thickness
max. range

## Slide 29: Interaction of β-particles with matter
β+ particles behave similarly as β- particles; they are ionizing and attenuated on their way through matter.
But at the end of the their attenuation one observes a pair annihilation with an electron, which yields high energetic γ-emission. Positrons are hence more dangerous than electrons.

## Slide 30: Bremsstrahlung
Bremsstrahlung (‘braking radiation’) is electromagnetic radiation produced by the deceleration of a charged particle when deflected by another charged particle, typically an electron by an atomic nucleus.
The moving particle loses kinetic energy, which is converted into a photon, thus satisfying the law of conservation of energy.
Bremsstrahlung has a continuous spectrum.

## Slide 31: Bremsstrahlung
Spectrum of the X-rays emitted by an X-ray tube with a rhodium target, operated at 60 kV. The continuous curve is due to bremsstrahlung, and the spikes are characteristic K lines for rhodium.
spectral distribution:
K = Kramer constant
I = electron current
Z = element number of material

## Slide 32: Bremsstrahlung
fit to data:
X0 is the radiation length. It is the mean distance over which a high-energy electron loses all but 1/e of its energy by Bremsstrahlung
Usual definition for the critical energy Ec (electron)
example: Pb (Z=82, ρ = 11.34 [g/cm3] → Ec = 7.34 MeV

## Slide 33: Synchrotron radiation
The electromagnetic radiation emitted when charged particles are accelerated radially (a ⊥ v) is called synchrotron radiation. It is produced, for example, in synchrotrons using bending magnets.
The energy loss of a charged particle (Z·e) due to radiation (during one cycle) is given by
with Z = element number, ε0 = electric field constant, R = radius of the storage ring, β=v/c and the Lorentz factor
For relativistic velocities β ≈ 1
It is apparent that one uses light particles to create synchrotron radiation.

## Slide 34: Synchrotron radiation
Raja Ramanna Centre for Advanced Technology
Indore

## Slide 35: Raja Ramanna Centre for Advanced Technology - Synchrotron radiation
Structure of a ribosome (components of a cell)
Applications: condensed matter physics, material science, biology and medicine.

## Slide 36: Typical range of radioactive radiation in air
range of 5.5 MeV α-particles in air is ~ 4.2 cm
range of 1 MeV β-particles in air is ~ 4 m
range of X-rays, γ-rays and neutrons is very large.
shielding or large distances (1/r2 law) are the solution

## Slide 37: Energy loss for electrons and positrons
e± are exceptional cases due to their low mass. They will be deflected significantly in each collision.
In addition to the energy loss due to ionization, the energy loss due to Bremsstrahlung is of importance.
For high energies the energy loss due to Bremsstrahlung is given by
and
Other particles like muons also radiate,
especially at higher energies.

## Slide 38: Bremsstrahlung
fit to data:
X0 is the radiation length. It is the mean distance over which a high-energy electron loses all but 1/e of its energy by Bremsstrahlung
Usual definition for the critical energy Ec (electron)
example: Pb (Z=82, ρ = 11.34 [g/cm3] → Ec = 7.34 MeV

## Slide 39: Comparison between electrons (β-) and positrons (β+) on their way through matter
β+ particles behave similarly as β- particles; they are ionizing and attenuated on their way through matter.
But at the end of the their attenuation one observes a pair annihilation with an electron, which yields high energetic γ-emission. Positrons are hence more dangerous than electrons.
electron
source
positron
source
detector

## Slide 40: Cherenkov radiation
Cherenkov radiation is emitted if the particle velocity is larger than the velocity of light in the medium.
symmetric orientation
no resulting dipole field
asymmetric orientation
resulting dipole field
change of dipole field → radiation
δ ≡ polarization of medium
atomic dipoles
fast orientation of dipoles
= 0.3071 MeV g-1cm2

## Slide 41: Cherenkov radiation
Pavel Alekseyevich
Cherenkov

## Slide 42: Cherenkov radiation
threshold velocity:
threshold angle:
Parameters of typical radiators
medium | n |  |  | 
air | 1.000283 | 0.9997 | 1.36 | 0.208
isobutene | 1.00127 | 0.9987 | 2.89 | 0.941
water | 1.33 | 0.752 | 41.2 | 160.8
quartz | 1.46 | 0.685 | 46.7 | 196.4
medium | n |  |  | 
air | 1.000283 | 0.9997 | 1.36 | 0.208
isobutene | 1.00127 | 0.9987 | 2.89 | 0.941
water | 1.33 | 0.752 | 41.2 | 160.8
quartz | 1.46 | 0.685 | 46.7 | 196.4
Note: Energy loss due to Cherenkov radiation very small compared to ionization (<1%)