## Slide 1: Neutral Particles

## Slide 2: Neutron detectors
Neutron detectors do not detect neutrons but products of neutron interaction!
James Chadwick, Nature 132 (1932) 3252

## Slide 3: Neutrons in Science …
Laboratory for fundamental physics: ElectricDipoleMoment
Ideal tool for probing matter:
  No Coulomb force: deep penetration
  Strong Interaction: isotope-specific detection
  Magnetic moment: magnetic structures
  Low energies: crystal structures
ultra cold neutron detection:
3He(n,p)3H

## Slide 4: … Technology
Neutrons can be used to produce energy
Biggest disadvantage: the (free) neutron is unstable:
Intense neutron sources require considerable efforts
  Reactors
  High-power low-energy accelerators
  Spallation sources
Fusion
Fission

## Slide 5: … and the world around
Cosmic Neutrons:
  Production in the atmosphere by galactic radiation
  Production on the sun
Neutron monitors:
Diagnostic for solar processes
Radiation protection at flight levels:
anticoin. shield
1 m2 scintillator
prop. counters

## Slide 6: Classification of Neutrons
de Broglie wavelength:

## Slide 7: General detection principle
Neutron detectors do not detect neutrons but products of neutron interaction!
external converter (radiator) converter = detector
Detection of a neutron is a sequential process
1. Interaction of the incident neutron: neutron transport
2. Transport of secondary particles to or within sensing elements
hadron, ion, photon transport
3. Primary ionization by secondary particles
4. Conversion to optical photons, gas amplification:
Transport of electrons and optical photons
5. Conversion to electrical signal

## Slide 8: The neutron detection process
Detection of a neutron is a sequential process:
  Interaction of the incident neutron: Neutron transport
  Transport of secondary particles to or within sensing elements: Hadron, ion, photon transport
  Primary ionization by secondary particles
  Conversion of optical photons, gas amplification:
  Transport of electrons and optical photons
  5. conversion to electronical signal S
These steps are described by transfer functions Ti(si-1,si)
Convolution of the Ti’s: Response function R(S,E)
… How to solve this integral equation?

## Slide 9: General detection principles
Basic requirements for neutron detection:
Slow neutrons: high Q-values, no resonances!
Fast and high-energy neutrons: large smooth cross sections!
Basic types of neutron detectors:
Neutron counters
  Signal does not depend on neutron energy
  Typical for detection of thermal neutrons
Neutron spectrometers
  Signal somehow related to neutron energy
  Inversion procedures are used to infer the neutron energy distribution

## Slide 10: Interaction of Neutrons
Indirect detection technique: induce neutrons to interact and produce charged particles.
Neutron detection and identification is important in the field of radiation protection because the relative biological effectiveness (quality factor) is high and depends on the neutron energy.

## Slide 11: Interaction of neutrons with matter
Neutron detectors can only be detected after conversion to charged particles or photons:
Elastic scattering: AX(n,n)AX → recoil nucleus AXZ+
Inelastic scattering: AX(n,n´γ)AX → recoil nucleus AXZ+ , e-
Radiative capture: AX(n,γ)A+1Y → e-
Neutron emission: AX(n,2n)A-1Y → radioactive daughter
Charged-particle emission: AX(n,lcp)A´Y → (lcp = p, d, t, α), recoil nucleus A´YZ+
Fission: n + AX → A1X1 + A2X2 + νn → fission fragments
cross section relevant
for neutron detection

## Slide 12: BF3 and 3He proportional counters
Cylindrical and spherical shapes
Large variety of sizes: I < 1 m
and pressures: p < 1 bar (BF3), 10 bar (3He)
Counters must be calibrated:
  3He and BF3 pressure ?
  10B enrichment ?
  Electrical field ?
  Wall effects ?
n/γ discrimination using a pulse-height threshold
BF3: aging at high dose rates
transport prohibited: HF formation!
3He: more efficiency than BF3 because of larger
low Q-value makes n/γ separation difficult

## Slide 13: BF3 and 3He pulse-height spectra
Wall effect: incomplete energy deposition by one ejectile:
Significant dead times:
Photon background suppressed by pulse-height threshold

## Slide 14: Neutron Detection
, Q=0.765 MeV
Moderate neutrons in spheres of different sizes and then detect the charged particles in a proportional counter in the center.
Bonner sphere

## Slide 15: Physics of organic scintillators
Unitary scintillators:
Benzene ring: delocalized π orbitals
Singlett (1X, 1X*, 1X**) and triplet (3X*, 3X**) states
Principal physical processes:
Excitation by electron impact, ion-ion
recombination, …
Non-rad. efficient internal degradation
1,3X**→1,3X*+ phonon
drain via competing channels:
quenching states
Rad. decay 1X* → 1X:
prompt fluorescence: τ = 1-80 ns, λfluor>λabs
Rad. transition 3X** → 1X* forbidden
Coll. deexc. 3X* + 3X* → 1X* + 1X* + phonon:
delayed non-exp. fluorescence: τ > 300 ns

## Slide 16: Ionization quenching and pulse-shape discrimination
Increased ionization density:
  More ion-ion recombination
  Ratio of 1X** and 3X** excitations increases
  Temporal concentration of transient
  quenching states (τ ≤ 100 ps)
Delayed fluorescence less dependent
on dE/dx than prompt fluorescence
Light yield dL(E)/dx is a non-linear function
Scint. decay depends on dE/dx
Pulse-shape discrimination
of particle species (Z,A)

## Slide 17: Pulse shape discrimination
Pulse shape discrimination (PSD) in organic scintillators are used in particularly liquid scintillators
(NE213 / BC501A)
PSD is due to long-lived decay of scintillator light caused by high dE/dx particle – neutron scatter interaction events causing proton recoil

## Slide 18: BEta deLayEd Neutron detector
BELEN-30 (90x90x80 cm3 PE)
20 3He counters (20 atm) outer ring
10 3He counters (10 atm) inner ring
efficiency (1 keV – 1MeV) ~ 40%

## Slide 19: Understanding the r-process

## Slide 20: β-delayed neutron emission

## Slide 21: Large Area Neutron Detector
Large Area Neutron Detector (2m x 2m x 1m)
neutron energy Tn ≤ 1 GeV
ΔTn/Tn = 5.3%
efficiency ~1
passive Fe-converter

## Slide 22: Reaction with Relativistic Radioactive Beams – R3B
Excitation energy E* from kinematically complete measurement of all outgoing particles

## Slide 23: Invariant mass analysis
Momentum reconstruction: (ħ=c=1)
four-momenta:

## Slide 24: Dipole strength distribution of 68Ni
O. Wieland et al.; Phys. Rev. Lett 102, 092502 (2009)
direct γ-decay
branching ratio:
Γ0/Γ = 7(2)%
D. Rossi et al.; Phys. Rev. Lett 111, 242503 (2013)
mean field calculation
E.Litvinova et al.; PRC 79, (2009) 054312
γ-ray decay data
neutron decay data
Pygmy resonance

## Slide 25: Neutrinos

## Slide 26: Neutrinos
Wolfgang Pauli

## Slide 27: Interaction of Neutrinos
;
;
(discovery of the neutrino)
Small cross section for MeV neutrinos:
Rate of solar neutrinos interacting in the Earth:
For high energies (GeV-range):

## Slide 28: Detecting the Neutrinos
Inverse beta decay:

## Slide 29: Discovery, Reines & Cowan 1956

## Slide 30: Solar Neutrinos

## Slide 31: First measurement of the solar neutrinos
Inverse beta-decay
(„neutrino-capture”)
600 tons
Carbon tetrachloride
Homestake Sun neutrino-
Observatory (1967-2002)
40 days neutrino irradiation …
Expected: 60 atoms 37Ar

## Slide 32: Super Kamiokande – Detection Concept

## Slide 33: Super Kamiokande – the Detector

## Slide 34: Super Kamiokande – the Detector