## Slide 1: Outline: From Ge(Li) to Germanium detector array
Lecturer: Hans-Jürgen Wollersheim
e-mail: h.j.wollersheim@gsi.de
web-page: https://web-docs.gsi.de/~wolle/ and click on
1960ties and 70ties: Ge(Li) detectors
1980ties: national HPGe detector arrays OSIRIS, HERA, TESSA
1990ties: EUROBALL and GAMMASPHERE
2000ties: position-sensitive Ge-arrays MINIBALL, EXOGAM, SEGA
under development: 4π γ-ray tracking arrays AGATA, GRETA

## Slide 2
Phys. Rev. 74 (1948) 100
H. Morinaga, P.C. Gugelot Nucl. Phys. 46 (1963) 210
(α,xn)
Invention of the NaI(Tl) detector 1948
Robert Hofstadter, after hearing about Callmann‘s work, started testing Tl activated alkali halide crystals. Na(Tl) was found to have the largest output

## Slide 3: Germanium transistor
1947
by
William Shockley,
John Bardeen and
Walter Brattain
(left to right)

## Slide 4: Early semiconductor devices
first transistor (Bell 1947)
hybrid circuits (1960)
first integrated circuit (1959)
Fairchild IC (1962)

## Slide 5
E. M. Pell 1960
Li-drifted n+ layer
p-type bulk material layer
Li-drift in p-type Si

## Slide 6: Gamma-ray interaction cross section
Photo effect: ~Z4-5, Eγ-3.5
Compton: ~Z, Eγ-1
Pair: ~Z2, increases with Eγ
100 keV – 2 MeV
is typical γ-ray energy range in nuclear science.
Compton scattering is dominant (in Ge)!

## Slide 7: First Ge(Li) detector: D.V. Freck and J. Wakefield
Milestone 1
Nature 193, 669 (1962)
Ge(Li) detector, active volume: 0.2 cm3
661.6 keV

## Slide 8
1963 Tavendale and Ewan (Chalk River)
Ge(Li) detector, planar: 2 cm3
ΔE = 6 keV at 1.3 MeV
use of a cooled FET reduced input noise to 0.7 eV (1965)

## Slide 9
Li-drift apparatus at IKP Cologne
First coaxial detector 1968 ΔE = 3.5 keV at 1.3 MeV 5.5 cm3

## Slide 10: The 1970ties
γ-spectroscopy with Ge(Li) detector
10 – 15 % rel. efficiency (Vol. 50-70 cm3)
resolution 1.9 – 2.3 keV at 1.3 MeV

## Slide 11: The “five-in-one“ Compton polarimeter (1974)
two concentric coaxial Ge(Li) detectors, outer detector 4-fold segmented
energy resolution 3.5 – 5 keV at 1.3 MeV

## Slide 12: Composite Ge-detectors
3(4) Ge(Li) detectors
in a common cryostat
1976
resolution 2.1 keV at 1.3 MeV
for 3 but not for 4 detectors

## Slide 13: First escape suppression spectrometer at Liverpool
John Francis Sharpey-Schafer

## Slide 14: The scattering problem
High background hence suppression shield
High efficiency hence arrays of Escape Suppressed Spectrometer

## Slide 15: Arrays of Escape Suppressed Spectrometers
TESSA0 the Escape Suppressed Spectrometer Array
The first one TESSA
Daresbury study weekend 1979
nuclei far from stability
UK Denmark collaboration
Niels Bohr Institute 1980-1982
FN tandem
5 Ge(Li), 5 NaI(Tl) suppression shields
γ2 factor of 8 improvement in ph. ph.
coincidences
no channel selection
TESSA1 14 element multiplicity filter

## Slide 16: TESSA0 the Escape Suppressed Spectrometer Array

## Slide 17: First Coulomb excitation experiments at UNILAC (1980)
208Pb (5.3MeV/u) → 235U
Doppler-corrected γ-ray spectrum for 235U
i13/2 proton and j15/2 neutron alignment in 235U and 237Np

## Slide 18: TESSA3, NORDBALL, 8π Spectrometer
BGO replaces NaI(Tl)
1 cm ≈ 1 inch
HERA (LBNL)
21 ESS (25% eff.) + BGO ball
γ-γ-γ coincidences
~ 1987
HERA at LBNL

## Slide 19: TESSA3

## Slide 20: Development of high-purity Ge at LBNL, Ortec, Umicore …
Production of Ge(li) detectors was abandoned after 1978 when high-purity Ge (HPGe) detectors became commercially available
Milestone 2

## Slide 21: High Purity Germanium detector

## Slide 22: HPGe detector – working principle

## Slide 23: HPGe detector – working principle

## Slide 24: HPGe detector – working principle

## Slide 25: HPGe detector – working principle

## Slide 26: HPGe detector – position sensitivity

## Slide 27: HPGe detector – position sensitivity

## Slide 28: The first case of a high spin superdeformed band

## Slide 29: GAMMASPERE 1993 Berkeley
110 Ge detectors (70% eff.)
escape suppression shields
70 detectors segmented into two halves to reduce the Doppler broadening
M.A. Deleplanque, R.M. Diamond eds Gammasphere proposal 1987

## Slide 30: EUROGAM II
24 CLOVER detectors with increased efficiency (130%) and improved granularity
F. A. Beck et al. Conf. Proc. 1994

## Slide 31: From EUROGAM to EUROBALL
γ-ray
γ-ray
Late 1980‘s:
Discussion of a cluster of seven detectors with large efficiency in add-back mode
Conclusion:
seven hexagonal detectors in a common cryostat
Encapsulated!

## Slide 32: The EUROBALL cluster detector
10 kg HPGE
rel. efficiency 600%

## Slide 33: EUROBALL-3 demonstrator at GSI 1993
GSI mass separator
efficiency: 19%

## Slide 34: Darmstadt-Heidelberg Crystal Ball and EUROBALL-3 demonstrator 1993

## Slide 35: EUROBALL 1997 - 2003

## Slide 36: EUROBALL (2003-2009) at RISING Rare ISotope INvestigation at GSI
4 g/cm2 Be
136Xe
exp(130Cd)~150 pb
750 MeV/u
variable
degrader
ΔE
implantation in Cu-plate or in 9 DSSSD
15 Cluster detectors with 105 Ge crystals
εγ = 11% at 1.3 MeV, 20% at 550 keV, 35% at 100 keV
very high γ-ray efficiency
high granularity (prompt flash problem)
S. Pietri et al., NIM B261 (2007), 1079

## Slide 37: EUROBALL at RISING stopped beam set-up (2006-2009)

## Slide 38: EUROBALL at RISING scattering experiment (2003-2005)

## Slide 39: 6-fold segmented, encapsulated MINIBALL detector
collaboration: Cologne,Heidelberg,Munich, Leuven

## Slide 40: Position-sensitive Ge-detectors (pulse shape analysis)
Milestone 3

## Slide 41
Miniball at
REX-ISOLDE, CERN
24 Ge-detectors in 8 cryostates, 6-fold segmented
abs. eff. 8.5%

## Slide 42: MINIBALL at REX-ISOLDE
Miniball at
REX-ISOLDE, CERN
24 Ge-detectors in 8 cryostates, 6-fold segmented
abs. eff. 8.5%

## Slide 43: Cluster and MINIBALL detectors at RISING 2005
70cm
20cm
beam
target

## Slide 44: Doppler broadening and position resolution
Position resolution
Angular resolution
Energy resolution
beam
projectile
g ray

## Slide 45: The idea of γ–ray tracking
Compton shielded Ge
Ge tracking array
Previously scattered γ-rays were wasted
Technology is available to track them
100
100
large opening angle
means poor energy
resolution at high
recoil velocity
combination of:
segmented detectors
digital electronics
pulse processing
tracking the -rays
EUROBALL/
Gammasphere
AGATA/GRETA
Milestone 4

## Slide 46: AGATA: Advanced GAmma Tracking Array

## Slide 47: AGATA detectors and AGATA triple-cluster
~2 kg
Signals from 36 segments + core
are measured as a function of time
(γ-ray interaction point)

## Slide 48: Ingredients of gamma-ray tracking

## Slide 49: AGATA: pulse shape analysis
Signals from 36 segments + core
are measured as a function of time
(γ-ray interaction point)
John Strachan

## Slide 50
LYCCA
Au, Be target
HECTOR BaF2 array
AGATA Cluster array
PreSPEC-AGATA campaign (2012)

## Slide 51
PreSPEC-AGATA campaign (2012)

## Slide 52: Doppler-shift correction – 238U on 197Au (386 mg/cm2) at 183 AMeV
66.372 | 79 Au | Kα3 | 0.033
66.991 | 79 Au | Kα2 | 27.5
68.806 | 79 Au | Kα1 | 46.4
77.577 | 79 Au | Kβ3 | 5.57
77.982 | 79 Au | Kβ1 | 10.70
80.130 | 79 Au | Kβ2 | 3.84
cos θγ
http://ie.lbl.gov/atomic/x2.pdf
Michael Reese

## Slide 53: Doppler-shift correction – 238U on 197Au (386 mg/cm2) at 183 AMeV
93.844 | 92 U | Kα3 | 0.099
94.654 | 92 U | Kα2 | 28.2
98.434 | 92 U | Kα1 | 45.1
110.421 | 92 U | Kβ3 | 5.65
111.298 | 92 U | Kβ1 | 10.70
114.445 | 92 U | Kβ2 | 4.15
cos θγ
http://ie.lbl.gov/atomic/x2.pdf
Michael Reese

## Slide 54: Scattering experiment at relativistic energies
Doppler effect
80Kr → 197Au, 150 AMeV

## Slide 55
HECTOR team

## Slide 57: AGATA at PreSPEC (GSI)
preprocessor
computer farm
digitiser
Damian Ralet,
Stephane Pietri
AGATA

## Slide 58: Summary